## Slide 1: FRC Robot Mechanical Principles
Review understanding from last week
  Robot agility and maneuverability?
  Chassis types & options
  Speed and Torque?
Torque vs. Speed
  Gear ratios
  Breakaway torque limit
  2 speed
  3 CIM vs. 2 CIM
  3 CIM + 2 Speed – vs. 3 CIM single speed
Wheels: Friction
Continuing Subjects:

## Slide 2: FRC Engineering/Design
Review:
Every year our Strategic Design has called for:
  “Fast, Stable, Maneuverable With Good, Pushing Power”
  How do you get maneuverable – agile – quick turning?
  How do you get stable?
  How do you get both?
  How do you get Fast?
  How do you get good pushing power?
  How do you get both?
Chassis & Drive train layout defined by middle of week 1?
An example of an 8WD
agile & stable tank drive layout

## Slide 3: Friction
Classical Friction Theory
Torque at wheel imparts a “Drive force” at wheel carpet contact point
This is reacted by a “Friction Force” of up to the “Friction coefficient” times the weight on the wheel
  The friction coefficient is a characteristic of the materials involved
  If the Drive force is greater than the Friction force, the wheels will slip
The maximum Torque that can be transmitted
by the drivetrain is the “Breakaway Torque”
that creates a Drive force equal the
Friction coefficient x Weight on wheel
= m * m * g
Weight = mass*gravity = m*g
Drive Force = Torque/radius
=m*m*g
Torque
Friction reaction force

## Slide 4: Drive Motors, Transmissions, Sprockets and Wheel Diameter
How to translate speed of motor to speed of robot?
  Motor speed inputs into transmission with a gear ratio
    Motor load results in speed loss
  Transmission output to sprockets connected by chain
    Ratio of sprocket teeth decreases speed
Overall Ratio includes motors, transmissions, sprockets/belts, wheel diameter
Wheel
Motor
Sprocket
Transmission

## Slide 5: Drive Motors, Transmissions, Sprockets and Wheel Diameter
Simple Transmission Gearbox (as in the CIMple Gear box)
  2 CIM motor input
65 teeth
14 teeth
14 teeth
5300 RPM
CIM Motor Free Speed
5300 RPM
CIM Motor Free Speed
Output Speed
= 5300 * 14/65
= 1150 RPM

## Slide 6: Basic Relationships - Review
Wheel / Transmission Mechanics
Torque = Radius x Force = T (in-lbs)
Rotational speed = w (rpm)
Velocity = v = (w*2*P*r)/(60 *12) (ft/sec)
Frictional Coefficient = m “empirical” – test wheel grip to carpet, with weight
Maximum Traction Force = FT = m x W (weight of the robot = mg)
Maximum Torque at wheel that can be transferred by friction
  Tm= m * W * radius
Max torque delivered by motor is at stall
Torque decreases with speed
w
Fw
Ft
T
r
W
v

## Slide 7: Drive Motors, Transmissions, Sprockets and Wheel Diameter
Wheel
Motor
Sprocket
Transmission
(RPM)
Velocity = v =
(w*2*P*r)/(60 *12) (ft/sec)

## Slide 8: COTS Drive Transmission Options

## Slide 9: Drive Motors, Transmissions, Sprockets and Wheel Diameter
Spreadsheet simulations allow quick iterations to explore different combinations of gearboxes, sprockets and wheel diameters.

## Slide 10: Gear Ratio Effects
Gear Ratio Optimization Trades Off Speed and Torque
Higher gear ratio
  Lower max speed
  More low end torque
  May not be able to use all of Torque?
Lower Gear Ratio
  Higher max speed
  Less max torque
  May not ever get to top speed?
Torque provides acceleration
  T = F * r = m * a * r
  increasing speed
Torque decreases with speed
Wheel friction limits amount of Torque that can be transmitted without spinning wheels
  Only get advantage of higher gear ratio if friction is high
  For Instance: m = 0.9 there is no advantage to a gear ratio above 7.3
For typical m = 1.1 What is optimum gear ratio?
Torque=>
<= Speed
<= Distance
m = 1.3
m = 1.1
m = 0.9
2CIMS in each of 2 single speed gearboxes
Time (seconds)

## Slide 11: Gear Ratio Effects
2 Speed Gearbox Allows Optimization of Speed and Torque
Torque=>
<= Speed
<= Distance
m = 1.3
m = 1.1
m = 0.9
2CIMS in each of 2 two speed gearboxes
Time (seconds)
Desire to “shift” when acceleration (or Torque) crosses
  Here shift from 11.43 ratio to 5.03 ratio at about 25 in-lbs and 16 fps
  Very slight advantage in distance / time
If m = 1.1 then get up to 320 in-lbs torque at low speed
And up to 15 fps!
Only is advantage if shifted at right times
Driver shifting is difficult
  Automation opportunity?
  Read speed on encoder and shift automatically?

## Slide 12: 2 CIM vs 3 CIM Drive
3 CIM / Gearbox Drive Eliminates Need For 2 Speed Gearbox
3 CIMs provide 50% more torque at any gear ratio
Minimal benefit for 2 speed gearbox
  Friction becomes more important than gear ratio
Can have ~14 fps robot (very fast) and have max transmittable torque
3 CIMs provide quicker acceleration – getting more distance vs. time.
  Equal to 2 CIM – 2 speed
Torque=>
<= Speed
<= Distance
m = 1.3
m = 1.1
m = 0.9
3 CIMS in each of 2 single speed gearboxes

## Slide 13: 2 CIM vs 3 CIM Drive
When May 3 CIM – 2 Speed Make Sense?
Low gear ratio – high speed
  High gear ratio set at level of max useful torque benefit
    and not trip breakers
    Here for m = 1.2, Ratio~ 9:1
  Low gear maintains high acceleration
  Makes difference only if accelerating over 15 feet distance
    At 20 feet may get up to
    3-5 foot advantage
    May not be controllable
Torque=>
<= Speed
<= Distance
m = 1.3
m = 1.1
m = 0.9

## Slide 14: Drive Simulation
Allows Convenient Evaluation Of Different Drive Train Configurations
Useful to understand trends
  But make sure to anchor to test data
Includes considerations for:
  Speed loss coefficient – how much slower motor is under load
    Free speed is 5300 RPM, loaded speed ~ 4300 RPM (81%)
    May be dependent on gear ratio – further test data needed
  Torque accelerates speed, but torque reduces with speed
  Speed desired called by voltage
  Voltage drops when load is first applied, current spike
Simulation
  Iterative time step solution - excel
  Test data can be taken to improve simulations
  Spreadsheets from team 33 and 148 (JVN) used and here-bye credited
    Modified both in calculations and display.