## Slide 1: Robot Mechanical Principles
Session Objectives:
Basic Drive Chassis Design considerations

## Slide 2: FRC Engineering/Design
Build Week 1:
Define Game Strategy
Define Robot Requirements – The “Strategic Design” spec.
Every year our Strategic Design has called for:
  “Fast, Stable, Maneuverable With Good, Pushing Power”
    Relative importance may vary
  Motor rules? 4 CIMs – 6 CIMs – How many should we use?
  What about wheel choices?
  Gearboxes? 1 speed or 2 speed? Gear Ratio ?
  What is terrain for the game? Bumps, platforms, ramps etc.
  The distance that the robot must sprint changes from year to year
Chassis & Drive train layout defined by middle of 1st week!

## Slide 3: Basic Relationships - Review
Wheel / Transmission Mechanics
Torque = Radius x Force = T (in-lbs)
Rotational speed = w (rpm)
Velocity = v = (w*2*P*r)/(60 *12) (ft/sec)
Frictional Coefficient = m “empirical” – test wheel grip to carpet, with weight
Maximum Traction Force = FT = m x W (weight of the robot = mg)
Maximum Torque at wheel that can be transferred by friction
  Tm= m * W * radius
Max torque delivered by motor is at stall
Torque decreases with speed
w
Fw
Ft
T
r
W
v

## Slide 4: Tank Drive
Most Popular Style of Drive Train in FRC
Two sets of wheels on each side of robot
  Drive independently
  Wheels are fixed angle
Turning performed by differential speed and sideways skidding of fore and aft wheels
Layout of wheels is critical to turning maneuverability
  Typically dropped ctr
6WD and 8WD most popular
  But typically designs have only 4 wheels touch ground at a time - How come?
Basic KOP C-base frame & drive set up from 2011/2012
2013 KOP

## Slide 5: Turning a Tank Drive
Right and Left motors spin fore and aft to generate twisting orque: T
Sideways reaction forces are from friction resistance to skidding
T = Fx * W – Fy * L
Fy = m*g*m = weight of robot x friction coefficient between tread and carpet
Fx maximum = m*g*m
If m (friction coefficient) is same for axial as lateral then:
  L<W in order to turn at all
  L<W/2 to turn smoothly
  What if m is different
    axial vs. lateral?
  Omni Wheel?

## Slide 6: Dropped Center Wheel(s)
Short wheelbase length needed for agile turning
Long overall wheelbase desired for stability
Dropped center wheel – 6WD with 6 inch wheels
Dropped center wheels
8WD with 4 inch wheels
Only 4 wheels touching carpet at a time
  Typically end wheels are about 1/8” above center wheel(s)

## Slide 7: 6WD & 8WD Tank Drive
Wheelbase Length to Width is Important
For agile turning with tank drive
  2.0 < X < 2.5 ratio of width to wheelbase length (of 4 wheels)
Game strategy will define aspect ratio of Robot (Length to Width)
Last year (2013) we used an offset 6WD raised front wheel (lower right)
As aspect ratio of robot goes from wide to long – may move to an 8WD
  Also for less rocking - control
Each has 4 wheels primarily on ground
Other wheels provide stability and engage when pushing
Low cg always important!
  Battery
  Motor/Gearboxes

## Slide 8: Wheel Diameter
Wheel Diameter
20% greater wheel base / stability
Generally smaller is better!
  Wheelbase, weight, packaging…
  Less gear reduction required
Unless game design requires larger diameter
  Even then consider other options
    2012 – d’Penguineers and other wedges.

## Slide 9: Off the Shelf Option
2012 VexPro Kit
Sheet metal construction
Available only in the long format
  31.5” x 25”
6wd or 8wd

## Slide 10: New 2014 Andy-Mark KOP Chassis & Drive Train
Pre-season notification – FRC Email 9-26-13:
“we can give you some general information about this year’s KOP Drive System. It will look very different from those of the past and the two major variations include the following: The C-Base is gone. In its place is a redesigned frame using sheet metal and extrusion designed to make it easier to attach superstructures to the drive base.
It is still a six-wheel belt drive robot, with an estimated final drive speed of about 10.5 feet per second. But, with the new design, we’ve changed to a direct driven center wheel powered by ToughBox Mini gearboxes.
The KOP Drive System can still be set up as a six-wheel drive “long robot”, but the redesign also now allows a six-wheel drive “wide” robot out-of-the-box. We are excited to continue to increase the competitive level of the KOP Drive System while continuing to give teams the opportunity to make the Kit of Parts as valuable as possible. We thank AndyMark and Gates Corporation for their support in creating this possibility.”

## Slide 11: New KOP Chassis
Layout and Drive Train for the 2014 AM KOP chassis
Wide or Long option – convertible – also assuming 112” perimeter rule stays
  2 choices of aspect ratio? (likely – due to different belt lengths required)
Tough-box mini 10.7:1 gear ratio = ~ 10.5 fps – 2 CIMs/in gearbox – 6” wheels
  6 inch wheels: 4 wheel wheelbase = L = (full robot length – 7” )/2
Wheelbase width = robot width minus 4” - wheel ctr to wheel ctr
  31 x 25 robot => 4w wheelbase: 12” , width: 21 , W/L = 1.75 - Not too agile
  25 x 31 robot => 4w wheelbase: 9”, width = 27”, W/L = 3.0 - Hard to keep straight
Frame height above ground is ~ 2”– implies smooth surface for game?
Top View
½ Robot
6WD, belt drive
Wide or long
Assume 2 sets of belt lengths(?) for 2 out of the box set-ups
W/2
L

## Slide 12: Upgrades on New KOP Chassis
What can we improve on? Some Possibilities:
Optimize our own width to length
Change to 4” wheels, Swap out toughbox mini for:
  Vexpro 3 CIM 6:1 ratio gearbox 12.5 fps, + full torque
  Or 2 CIM with shifter gearbox (~15 & 62 fps)
  8WD or 6WD layouts possible
  Overall wheel base length is overall length – 5” (10% better than KOP)
Drop Frame to 1” height above carpet (lower c.g.)
Top View
½ Robot
6WD
8WD

## Slide 13: AM KOP Frame & VexPro KitBot & 80/20
Chassis Requirements
Able to convert from wide to long format and any in between (24:31  31:24)
Able to handle 8WD, 6WD, with 4” or 6” wheels.
Able to integrate 2 (or 3?) likely drive train choices (others also possible)
  4 CIM drive motors into 2 two-speed transmissions (COTs transmission)
  6 CIM drive motors into 1 speed transmission (COTs or custom?)
  4 CIM swerve drive system (mix of COTs and custom)
Agile and smooth turning capability
Best balance of speed and pushing power
  ability to change ratios without too significant effort (1 hour)
Lowest possible c.g.
Maximize stability
Able to attach a superstructure
Easily attach securely and detach bumpers
Weight <40 lbs.

## Slide 14: Some Frame Options
Design needs to be within our manufacturing ability and be easy to maintain
  change wheels, transmissions etc. - within 20 minutes!
  KOP (Andymark)
    Old KOP no longer provided – new sheet metal kit-bot
    New KOP – modified (aka “Kitbot on Steroids”)
  80/20
    We have experience with material – Miss Daisy style or variant
    Bearing blocks are interesting for tensioning
  Vexpro kit-bot
    Specific robot aspect ratio – may not align with strategy
    Otherwise well made – 558 used it in 2013 – positive reports
Custom – have prototype developed in the Fall
  Bumpers – generally a sort of afterthought
    Maybe optimize and easy on/off, strong system in Fall?
    Team 33 Killer Bee approach – Bumper provides strength of frame
Requirement: Must have chassis up and running by end of week 2
  Otherwise will not achieve other game goals